## Slide 1
1
The French Energy & Climate Strategy and the Future Role of Nuclear Electricity
Carole Mathieu, Ifri Centre for Energy
Bruegel, 15/05/19
Notes: 1

## Slide 2
2
French energy consumption by vector, 2015, 2030 and 2050
Targeting net zero emissions by 2050
Carbon neutrality implies a very sharp drop in energy consumption following strengthened EE efforts and a supply mainly composed carbon-free electricity, bioenergies and renewable heat
Chart: TWh
| 2015 | 2030 | 2050
Electricity | 490 | 520 | 600
Biomass | 90 | 140 | 120
Biofuels | 30 | 40 | 60
Renewable gas | 5 | 30 | 200
Renewable Heat | 15 | 55 | 80
Natural gas | 470 | 345 | 0
Oil products | 820 | 470 | 30
Coal | 130 | 30 | 0
Energy saving | 0 | 420 | 960
Source: Draft SNBC
Notes: 2
(47.5% of total installed capacity)

## Slide 3
3
Final energy consumption, 2010-2028
Policy actions to reduce final energy consumption in all sectors (by 2028)
MAIN POLICY MEASURES
Carbon pricing (€86/t in 2022)
2.5 million homes renovated by 2023
Public support for high-performing heating systems
White certificate scheme beyond 2021
EU emission standards in the automotive sector + support to car-sharing
Final energy consumption to decrease by 7% in 2023 and by 14% in 2028 compared to 2012 levels
Chart: TWh
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
a | 1645 | 1677 | 1668 | 1661 | 1651 | 1655 | 1628 | 1643
b | 1643 | 1625.8 | 1608.6 | 1591.4 | 1574.2 | 1557 | 1540 | 1516 | 1492 | 1468 | 1444 | 1420
Source: Draft PPE
Notes: 3
(47.5% of total installed capacity)

## Slide 4
Nuclear, the backbone of the French electricity system
4
63.1 GW installed nuclear capacity
393.2 TWh of nuclear electricity produced in 2018
≥90% decarbonized electricity mix
Retail electricity prices about 15% lower than EU average for households (€0.1754/ KWh)
Chart: mix
| Nuclear | Thermal generation | Wind | Solar | Hydro | Bioenergy
 | 0.717 | 0.072 | 0.051 | 0.019 | 0.124 | 0.018
French electricity production by source, 2018
Source: RTE, bilan 2018
Location of the 58 operational nuclear reactors
Capacity | Number of reactors
1450 MW | 4
1300 MW | 20
900 MW | 34
1650 MW (under construction) | 1 (mid-2020)
Source: EDF, 2019
Notes: 4
(47.5% of total installed capacity)

## Slide 5
Towards a more diversified electricity mix
5
Expected changes in gross electricity production
Source: Draft PPE
Chart: TWh
| 2017 | 2023 | 2028 (A) | 2028 (B)
Nuclear | 379.2 | 393 | 382 | 371
Coal | 9.7 | 0 | 0 | 0
Natural gas (and oil) | 44.1 | 34 | 32 | 32
Hydro | 53.6 | 62 | 62 | 62
Wind | 24.1 | 63 | 96 | 100
Solar PV | 9.2 | 24.5 | 43 | 53
Bioenergy | 9.5 | 9 | 9 | 10
50% nuclear target shifted to 2035 climate protection comes before the diversification goal
CAPACITY CLOSURES
Fessenheim (2 reactors) to be closed by Spring 2020
All four coal stations (35% of CO2 emissions from the power sector) to be closed by 2022, unless adequacy issues
2 nuclear reactors to be closed in 2027-2028
Possibly 2 additional reactors to be closed in 2025-2026 (decision in 2023) IF the regional context is favorable
50% nuclear by 2035  closing 14 reactors in total
Notes: 5
Official target for renewables: to reach 40% of total electricity production by 2030 (compared to 17% today)
  2023: 27% renewables / 67% nuclear
  2028: 33-36% renewables / 59-61% nuclear
Complementarity with renewables: 2/3rd of existing French reactors can go from 100 to 20% capacity in 30 minutes

## Slide 6
Extending the technical life-time of reactors, while planning a gradual decommissioning
6
French nuclear capacity (GW) assuming a 40 year technical lifetime
Source: EDF
On average, French reactors are 31 years old
75% of all French reactors will reach the 40 years threshold by 2030
« GRAND CARENAGE » : Investment programme to modernize existing reactors and ensure a safe and high-performing operation beyond 40 years, with the approval of the Nuclear Safety Agency
  €4bn/yr over 2014-2025
  4th ten-year inspection to start with the 900MW reactors, in 2019 for Tricastin
Assuming a max. 60 yr technical life-time, 50GW of nuclear capacity will have to be put offline by 2050  a gradual phase out is necessary to avoid a cliff-edge effect
Notes: 6
All reactors have been built over 25 years

## Slide 7
Building new reactors : a topic for the next Presidential campaign
7
Beyond 2030-2035, new decarbonized electricity production means will have to be built:
  Renewables + storage and other decabonized flexibility sources ?
  Renewables + new nuclear ?
Keeping the nuclear option « open », what implications?
  Maintaining the industrial capacity after EPR I
  Long delivery time: close to 10 years needed between the decision and the commissioning of the first pair of reactors, then 1 reactor could be commissioned every 1-2 years (EDF)
By mid-2021, the government will gather « all elements needed » to take an informed decision on the need to build new nuclear reactors
Notes: 7

## Slide 8
Key factors weighing in future decision
8
Commissioning of Flamanville EPR by mid-2020 / implementation of Hinkley Point C project
Ability of the French nuclear industry to define a competitive « EPR2 » offer & to define a robust waste management strategy
Industrial sovereignty dimension:
  Nuclear: French industry spanning the full range of nuclear activities, 220 000 jobs, mostly highly-qualified
  Nuclear exports / Sino-Russian duopoly / non-proliferation strategy
Regional / EU dimension:
  Influence of neighbouring countries’ experience, including the success of Germany’s Energiewende and coal phase out plan
  Approval by the EU Commission will be necessary for a new remuneration / risk-sharing scheme
  EU debate over carbon neutrality by 2050
Notes: 8
Standardization of key components, digital engineering, simplified design to improve constructability.
Existing nuclear waste storage sites have been designed for the existing fleet, with the assumption that reactors will have an operational life of 50 years.

## Slide 9
Centre Énergie – Centre for Energy
Carole Mathieu, Head of EU Energy & Climate Policies
mathieu@ifri.org
27, rue de la Procession, 75740 PARIS CEDEX 15 Tél. +33 (0) 1 40 61 60 00 • Fax : +33 (0) 1 40 61 60 60
www.ifri.org
9
Notes: 9